## Slide 1
Components of cost
Prime cost
Factory cost
Office cost
Total cost
1. Prime cost or Direct cost = Direct material cost +Direct labour cost + Direct expenses
2. Factory cost or works cost = Prime cost + Factory expenses
3. Office cost or Manufacturing or Production cost = Factory cost + Administrative expenses
4. Total cost = Office cost + Selling expenses + Distribution expenses

## Slide 2
Selling Price : If the profit of factory is added in the total cost of product it is called selling price.
So the customers gets the article by paying the price which is named as “ Selling Price.”
Selling Price = Total cost + Profit or Loss

## Slide 3
Selling Price : If the profit of factory is added in the total cost of product it is called selling price.
So the customers gets the article by paying the price which is named as “ Selling Price.”
Relation between the elements of cost and components of cost is illustrated as :

## Slide 4
Allocation of overheads (or Indirect expenses or oncost)
1 .Factory expenses
2. Administrative
3.Sales and distribution Expenses
Most of the overheads of above categories can easily be found out from records.
But some overhead charges require good knowledge and experience of the estimator. These are following :-
1. Depreciation
2. Obsolescence
3. Interest on capital
4. Idleness
5. Repair and maintenance

## Slide 5
Depreciation
Efficiency and value of machine or asset reduces with the lapse of time during use, which is known as Depreciation.
So some money must be set aside yearly from the profits, so that when the equipment becomes uneconomical, it can be replaced by the new one.
Therefore, the initial cost of machine + installation charges + repair charges – scrap value is charged against overheads and spread over the machine’s useful life.
For this purpose depreciation account is opened in the Company’s books known as “Depreciation” or “Sinking Fund “
and is deducted yearly from the profit and kept separate to have sufficient money for replacement at end of useful life.

## Slide 6
2. Obsolescence : is the depreciation of existing machinery or asset due to new and better invention, design voluntary euipment or process etc. Although the old machine is efficient but becomes out of fashion and uneconomical due to new better machine which has come in the market.
It is very difficult for estimator to provide for the on cost on obsolescence, because no body can say when are revolutionery change is coming in the market.
But is a general practice to reduce the life of machine so as to account the effect of obsolescence.
Now the depreciation and obsolescence charges are calculated on reduced life.

## Slide 7
Example
Expected life of machine = 25 years
Then the Depreciation rate = 100/25 = 4%
By considering obsolescence also, its life may be taken as 20 years
Then the combined depreciation and obsolescence charges will be 100/20 = 5% instead of 4%
Therefore, the difference 5-4 =1% will be obsolescence charges.

## Slide 8
The other causes of depreciation are physical decay, accidents, deferred maintenance and neglect, inedequacy etc.
Depreciation can be classified as under :
1. Depreciation due to physical conditions :
Wear and tear
Physical decay
Accidental
Deferred maintenance and neglect
2. Depreciation due to Functional causes :
Inedequacy
Obsolescence

## Slide 9
a. Depreciation due to Wear and tear :
Wear and tear of certain components takes place despite sufficient precautions i. e. proper lubricating and cooling , which minimize wear and tear. So the cost of replacement
Indicates importance of depreciation due to wear and tear.
b.Depreciation due to physical decay :
insulation of materials, furniture, electric cables, buildings, chemicals and vessels which gets decay, because of climatic and atmospheric effects, - result in reduction of value (there by reduction of cost) of such articles with lapse of time.

## Slide 10
c. Accidental Depreciation :
may occur due to some wrong operation, or some loose component or some other cause which may result in damage.
Nowadays most of the owners get their equipment insured , pay certain premium periodically depending upon the estimated cost and life of equipment.
Depreciation due to Deferred maintenance and ignore :
Every manufacture supplies certain instructions for the smooth and efficient running of an equipment. If these instructions are not properly followed because of poor maintenance and neglect; then the life of equipment may be reduced and result in depreciation due to this cause.Ex. vehicles

## Slide 11
e.Inedequacy :
means reduction of efficiency of an asset ; fall in efficiency; result firstly , even if any equipment servicing under proper precautions and sufficient maintenance is provided, there is fall in efficiency with the lapse of time.
Secondly suppose after 2-3 years of running, the demand of products manufactured by certain plant is increased. But the plant cannot cope up with the increased demand. This needs additional money either to replace with the bigger size machinery or installation of the similar size more plants. This is ,what is called depreciation due to inedequacy.