## Slide 1
SIMPLIFICATION
Means making improvement in methods by
Eliminating unnecessary parts
Rearranging other elements of the job and making them easier and safer to perform
It is the process of reducing variety of a product by limiting product range, their types, sizes, design and/or type of material
Reducing complexity of manufacturing process
Difficult in highly styled items because their styles are changing very rapidly specially for the items used by ladies and children
Due to lack of simplification ,some people do not like to purchase foreign products
Classification and coding help locating and identifying all items( i.e., products, components etc.)
The availability of suitable standards assist in simplification

## Slide 2
Advantages
To Manufacturers
Use of special purpose machines and tools is possible
Less capital is blocked in raw materials, finished products, jigs, dies and other special tools
Less supervision is required
Less chances of errors
Manufacturing cost reduces because less variety -> large number of products of same variety are produced
Correct estimation is possible
Less chances of obsolescence

## Slide 3
Training to worker become easy , quick and economical
Increased production rate
Lower unit cost
Investment of capital will be less
Standardisation is possible, which raises quality of product and products of uniform acceptable quality will be available in the market
Reduces wastages of labour and material
Reduction of error in shipment
Prompt delivery
Continuous employement instead of temporary when this or that size of model was needed

## Slide 4
(ii) To Distributors
Selling is easy because only few items are to be sold
Less capital is blocked in keeping less variety of products in hand
Less depreciation and obsolescence of products in products in stock
Selling expenses are reduced because of less handling
Accounting and other clerical work reduced
Less storage space is required
Elimination of slow moving stock
(ii) To Consumers
Better quality of products is available
Better services in delivery and repairs
Confidence in purchase

## Slide 5
STANDARDISATION
Setting up of standards for quantity, quality, raw material, size and performance etc. of any product
It is done after considering various scientific procedures and helpful for checking quality of any product
Simplification is the selection of those items which are of greatest demand and eliminaton of other items ,while standardization is to set standards for that simplified item
The standards fixed should give best method, specification and the type considering all the factors such as available equipment, working conditions, material and tools etc. all being standardized
Ex number of threads on specific size of bolt / stud

## Slide 6
Standardisation Procedure
With the help of market research, sales statistics etc. , decide what to sell in future
Then, define a range of product
From the range ask designer to develop minimum variety of components to match the range
Introduce new materials, components etc., if necessary.

## Slide 7
An approach to standardisaton necessitates the classification of materials and component parts.
Classification
Classification aims at, systematically, grouping items together by their common features and subdividing them by their special feature
A system of classification and coding is necessary for the design of new products within the range defined
Such a system should readily :
Identify and locate identical items in new designs
Facilitate the use of standard items
Identify substitutes in case of stock outs
Help developing group technology
Aid to improve parts location in the store

## Slide 8
Classification procedure involves the following steps :
Define all items
Classify each item according to its basic characteristics
Identify each item by allocating to it some meaningful code number
A code consists of letters and numbers. The aim is to classify from general to particular
Ex. Grinding Wheels- various wheel features are denoted by letters and numbers. A code is marked on grinding wheel.
According to Bureau of Indian Standards ( formerly Indian Standard Institution) is specified as follows :
G C 54 g 6 V BE
Green Silicon Medium Soft Dense Vitrified Suffix
(Prefix) carbide grain grade structure bond (Trade secret) Depends upon
abrasive size the process and type of manufacture

## Slide 9
Advantages of Standardisation
Design department :
Fewer specifications, drawings and part lists have to be prepared and issued
Thus more time is available to develop new designs or to improve established designs
Better resources utilisation
Allocation of work to suit available talent
Lesser design mistakes and design alterations
Less qualified personnel can handle routine design works
2. Manufacturing department :
Lower unit cost
Better quality products

## Slide 10
Accurate delivery dates
Better methods and tooling
More effective trainings
Better services of production control, stock control , purchasing etc.
Fewer tool changes and process setups
Increased interchangeability of parts
Better utilisation of manpower and equipments
Longer production runs with fewer change over
The operations can be analysed and broken easily into short repetitive cycles which can easily be mastered

## Slide 11
3. Marketing department
Better quality products of proven design at reasonable price  greater sales volume
Increased margin of profit
Less pressure of aftersales services
Better product deliveries
Easy availability of spare parts
4. Production planning section :
Scope for improved methods, processes and layout
Opportunities for more efficient tool design
Greatly reduced pre production planning activities. Fewer issues of new planning cards

## Slide 12
5. Production control department :
Well proven design and methods improve planning and control
Chasing small batches(of products) consumes less time
Fewer delays arise from waiting for materials, instructions, tools etc.
Accurate delivery promises
6. Purchase and stock control section :
Holding stock of standard items(i. e. less variety of matrials and components0 -> less paper work and fewer requisitions and orders
Storage and part location can be improved
Large purchase quantities -> favourable purchase contacts
Newer control techniques can be used for better stock control of stock

## Slide 13
7. Quality control department :
Better inspection and quality control
Operators become familiar with the work and produce jobs of consistant quality
Quality standards can be more clearly defined
8. Work –study section:
Effective break down of (limited) operations into short repetitive cycles and effective work measurement afford considerable opportunities for work study
9. Supervision :
All the above points help the supervisior
Less time is wasted in resolving production snags such as wrong information, faulty toolings etc.
Reduced rejections and scrapes

## Slide 14
More time is available to make useful records and preserve statistics
10. Costing :
Better control by installing standard costing
Disadvantages of Standardisation :
Reduction in choice because of reduced variety and consequence loss of business or customer
Changes in public taste seriously affect a company producing only standard product range
Difficult to introduce new models because of less flexible production facilities and due to the cost of specialised production equipment
Standardisaton tend to favour large companies, because small or new concerns can rarely get much business even by producing same price as the big companies

## Slide 15
Standards ones set, resists change -> may become an obstacle to progress
Applications of Standardisation
Finished products, e.g. cars and televisions
2. Subassemblies and components, e.g. automobile gearbox and to electric bulbs
3. Material standardisation, e. g. both of direct material(plain carbon and alloy steels, arc welding electrode core wires, etc.) and indirect materials (such as oils and greases)
4. Production equipment standardisation, e. g. that of machine tools, presses, welding equipments etc.

## Slide 16
International Standardisation
For export market
International Organisation for Standardisation (ISO)
ISO does not issues independent standards of its own but it makes recommendations which are included in the national Standards of the collaborating countries
National standardisation :
Every country has its own standards. IS in India, BS in UK, DIN in Germany are few examples of national or home standards

## Slide 17
Diversification
Concept
Contrary to simplification
means(i) addition of new products or (ii) introduction of established products into new markets
Tends to increase complexity of the methods of manufacturing, because sometimes consumer like to have variety in type, size, colour and quantity of products being manufactured. This adds to the cost characteristics of production which is of varied nature.
The extent of to which the diversificaton programme can be carried out must be determined by market analysis of probable volume at varying lavels of diversification compared with production cost of the volume obtainable at those various lavels.

## Slide 18
Industries generally expand. An automobile concern may think in terms of diversifying in its own product lines, an aircraft concern may like to expand in field of propulsion or electronics and so on.
Diversification adds to the classes of consumers served, by developing new technical knowledge.
Reasons for diversification :
Survival
To offset declining or vanishing market
To obsolete facilities
To offset offset declining profit margins
To compensate for technical obsolescence
(B) Stability
To offset seasonal slumps
To offset cyclic fluctuations
To balance between high margin and low margin products
To maintain market share
To meet new products of competitors

## Slide 19
(B) Stability
To offset seasonal slumps
To offset cyclic fluctuations
To provide balance between high margin and low margin products
To maintain market share
To meet new products of competitors
To tie customers to the firm
To distribute risk by serving several small markets
To develop a strong competitive supply position by offering several close substitute products

## Slide 20
(C) Productive utilisation of resources
To utilise waste or by-products
To make use of basic raw material
To utilise excess productive capacity
To make use of innovations from internal technical research
To make full use of management resources
To capitalise on a firm’s market contacts
(D) Adaption of change in customer needs
To meet the demands of diversified dealers
To meet specific requests of important groups of customers
To improve performance of existing products through adding accessories

## Slide 21
(E) Growth
To counter market saturation on present products
To reinvest earnings
To take advantage of usually attractive opportunities
(F) Miscellaneous
To maintain reputation of industrial leadership
To realise maximum advantage from the tax structure
To comply either desires of owners or management
Possibly the easiest route of diversification is through merge or acquisition